# SIW TAC Scientific Calibration report

Applicable documents, AD-1 : MYO-SIWTAC-Cal/Val Plan, V1.0, 21. June 2010

# Regional Sea Ice Antarctica

## Overall description of calibration task

AD-1: The objective of the calibration is to perform verification of the SIW TAC products before release of the products into the V2 portfolio.

- For existing products which are introduced into the TAC, the aim of the calibration is: To verify that the production gives the expected results and that this is disseminated correctly.

- For new developed products a systematic analysis of the quality is necessary. Calibration is performed by comparison with high quality reference data set in a limited time period.

The high resolution regional sea ice edge product for the Antarctic is a new product provided by BAS. It covers the Antarctic Peninsula and Weddell Sea region in the Southern Ocean, between 50(S-90(S and 0(W-90(W. The products are provided every working day.

The calibration will be:

- Verify that the products are gridded correctly and CF-1.4 compliant.

- Comparison with gridded ice edge position information obtained by manual interpretation of MODIS optical satellite imagery.

- Comparison with gridded OSI SAF sea ice edge product (Eastwood, S. (Editor) (2009) Ocean & Sea Ice SAF Sea Ice Product Manual, Version 3.6, http://saf.met.no/docs).

## Description of calibrated system

The Antarctic high resolution regional sea ice edge product is an operational product from BAS that is delivered to MyOcean. The product is based on manual interpretation of satellite SAR data from Envisat Wide Swath Mode ASAR imagery. The nominal temporal span between interpreted swaths is 24 hours and the nominal product grid resolution is a 1km. The Envisat data are in wide swath mode (WSM) with a swath width of 450 km and are resampled to a spatial resolution of 100 meters. The temporal coverage is variable and focused on the austral summer season (October to March). The sea ice product’s spatial extent depends on data availability.

| Product Lines | BAS-ANT-SEAICE_TYPE-L4-NRT-OBS |
| --- | --- |
| Geographical coverage | 0 W  90°W ; 50°S  90°S |
| Variables | Sea ice edge position |
| Available time series | From October 2011 – on going |
| Temporal resolution | Daily analysis / irregular |
| Target delivery time | Daily on working days before 14 UTC |
| Horizontal resolution | 1 km |
| Format | Netcdf CF1.4 |

The NetCDF-files are finally transmitted to the SIW-TAC Dissemination Unit at met.no. A verification of the data content and quality has been performed. The netCDF file is checked against the CF-Convention compliance checker for NetCDF format developed at the Hadley Centre for Climate Prediction and Research, UK Met Office by Rosalyn Hatcher. The checker can be found at http://titania.badc.rl.ac.uk/cgi-bin/cf-checker.pl

Calibration of the ice classification product is difficult due to lack of in situ observations and coincident high resolution imagery for comparison. As a alternative the product will be compared with a manually interpreted sea ice edge from MODIS satellite imagery and the OSI SAF sea ice edge product.

## Difference between calibrated system and operational V2 system

There are no differences between the current system that has been calibrated and the expected operational V2 system for global sea ice products.

## Calibration results

### NetCDF compliance check

Output from the compliant check of a sample NetCDF file ( ice_edge_hr_sh_20110730_043634_4.nc):

CHECKING NetCDF FILE: /tmp/30184.nc

=====================

Using CF Checker Version 2.0.2

Using Standard Name Table Version 16 (2010-10-11T12:16:51Z)

Using Area Type Table Version 1 (5 December 2008)

------------------

Checking variable: crs

------------------

------------------

Checking variable: ice_edge

------------------

------------------

Checking variable: xc

------------------

------------------

Checking variable: yc

------------------

------------------

Checking variable: lon

------------------

------------------

Checking variable: time

------------------

------------------

Checking variable: lat

------------------

ERRORS detected: 0

WARNINGS given: 0

INFORMATION messages: 0

### Comparison with MODIS satellite imagery

Given the lack of in situ observations we used MODIS satellite imagery for comparison with the BAS-ANT-SEAICE_TYPE-L4-NRT-OBS product. The MODIS satellite imagery has a pixel spacing of 250m which is similar to the Envisat ASAR resolution. MODIS satellite imagery is obtained from the NASA LANCE website (http://lance.nasa.gov/imagery/rapid-response/) which provides access to near real time MODIS data products. We examined images available during the first three months of 2011 and identified 16 instances of cloud free MODIS imagery which overlap pre-operational MyOcean products. For each instance the difference between acquisition times is less than 12 hours. Both the ‘true colour’ (bands 1-4-3) and ‘false colour’ (bands 3-6-7) middle-infrared product are used.

An example of the MODIS 3-6-7 product and corresponding ice edge product are provided below in Figure 1 and Figure 2. The spatial extent of the MODIS calibration product matches the spatial extent of the corresponding Envisat ASAR image used to create the MyOcean product. Figure 3 shows the location of this example product.

Figure 1: MODIS 3-6-7 image product

Figure 2: Interpreted ice edge from MODIS image

Figure 3: Location of MODIS image example in Figures 1 & 2

The MyOcean and MODIS sea ice products were compared using methodology established during an Eumetsat OSI SAF visiting scientist scheme (CDOP-SG07-VS01) comparing MyOcean sea ice edge product with the OSISAF sea ice edge product (see section 4.3). This methodology is described in the final report (see section 4.3 for reference). To account for similar resolution of the MODIS and ASAR images, the comparisons were performed on a 1 km grid.

The statistical parameters derived from this analysis include:

- Average pixel classification agreement

- Average distance from MyOcean ice edge to MODIS ice edge

- Average distance from MODIS ice edge to MyOcean ice edge

These results are presented below.

| MyOcean product | Agreement (%/100) | Average MyO – MODIS distance (pixels) | Number of pixels comprised in MyO ice edge | Average MODIS – MyO distance (pixels) | Number of pixels comprised in MODIS ice edge |
| --- | --- | --- | --- | --- | --- |
| ice_edge_hr_sh_20110113_021245_2.nc | 0.967 | 2.204 | 735 | 2.308 | 868 |
| ice_edge_hr_sh_20110114_063311_4.nc | 0.95 | 2.098 | 1023 | 2.014 | 1069 |
| ice_edge_hr_sh_20110115_055843_3.nc | 0.739 | 3.768 | 536 | 3.462 | 592 |
| ice_edge_hr_sh_20110118_122137_3.nc | 0.961 | 1.24 | 435 | 0.992 | 440 |
| ice_edge_hr_sh_20110123_060458_3.nc | 0.913 | 2.472 | 1500 | 3.591 | 1675 |
| ice_edge_hr_sh_20110124_134238_2.nc | 0.99 | 2.154 | 930 | 2.394 | 965 |
| ice_edge_hr_sh_20110128_030409_3.nc | 0.966 | 3.067 | 361 | 3.392 | 446 |
| ice_edge_hr_sh_20110129_072859_1.nc | 0.971 | 1.095 | 502 | 1.148 | 524 |
| ice_edge_hr_sh_20110210_032730_3.nc | 0.949 | 4.721 | 475 | 5.448 | 451 |
| ice_edge_hr_sh_20110214_024135_2.nc | 0.973 | 9.987 | 166 | 8.995 | 154 |
| ice_edge_hr_sh_20110301_033109_3.nc | 0.964 | 11.238 | 611 | 9.962 | 510 |
| ice_edge_hr_sh_20110313_025215_2.nc | 0.978 | 10.816 | 324 | 11.245 | 295 |
| ice_edge_hr_sh_20110314_021541_1.nc | 0.929 | 4.995 | 601 | 4.258 | 501 |
| ice_edge_hr_sh_20110315_031817_3.nc | 0.946 | 5.449 | 1115 | 4.281 | 844 |
| ice_edge_hr_sh_20110326_063245_3.nc | 0.908 | 4.745 | 717 | 4.589 | 692 |
| ice_edge_hr_sh_20110330_022935_1.nc | 0.976 | 9.211 | 540 | 8.455 | 440 |

These results are based on a small number of comparisons due to difficulties in finding cloud free MODIS imagery which corresponds with MyOcean sea ice edge products. This sample size will be increased as more match-ups are identified. We intend to update this calibration report at the end of the austral summer (April 2012).

In general the classification agreement is very good and greater than 90% in all but one instance. The distance between ice edges varies between 1 and 11 pixels. The separation is likely correlated with gap between acquisition time of the MODIS and Envisat ASAR images. This will be investigated later with a larger sample size.

### Comparison with OSISAF sea ice edge product

The MyOcean and MODIS sea ice products were compared during a Eumetsat OSI SAF visiting scientist scheme (CDOP-SG07-VS01) during 2011. The aim was to compare MyOcean high resolution (1km grid) sea ice edge for the Antarctic against the coarser resolution (10 km grid) OSISAF sea ice edge product. The method and results are described in the final report (OSI SAF Product Validation Report - The Southern Hemisphere Sea Ice Products, V1.0, 2011).

The results show general good agreement and a summary is presented below.

| Parameter | Jan | Feb | Mar | Jun | Jul |
| --- | --- | --- | --- | --- | --- |
| Sample number per month | 52 | 39 | 57 | 73 | 65 |
| Average pixel classification agreement (%/100) | 0.915 | 0.944 | 0.947 | 0.971 | 0.951 |
| Average distance from MyOcean ice edge to OSI SAF ice edge (pixels, 10 km pixel size) | 1.82 | 1.33 | 1.41 | 0.985 | 1.24 |

## Calibration technical summary

Production Centre:

SIW-BAS-CAMBRIDGE-UK

Calibration task:

The product is checked for compliance with NetCDF/CF-1.4 convention, and is compared to a similar sea ice product produced manually from MODIS satellite imagery and with OSI SAF sea ice edge product.

Calibration summary:

The NetCDF product complies technically with the CF-1.4 convention.

Validation is a challenge due to limited available relevant in situ measurements and small number of cloud free coincident MODIS images. However based on the small sample size currently available (16) the agreement is generally good.

Andrew Fleming & Andreas Cziferszky, British Antarctic Survey, October 2011